cONTRIBUTION:	NTCO0347                                      FEB. 28, 2006

working Group:	Network Working Group

TITLE	Default IP-to-IP interconnection parameters example scenario

Issues Addressed:

This contribution proposes an IP-to-IP interconnection interface guideline definition approach, encouraging bilateral IP-to-IP interconnection scenarios, while ensuring that minimum interface specifications can be met in situations where such bilateral agreements cannot be achieved.

Source:	Cogeco Cable INC.

AUTHOR:	Louis Bourbeau
louis.bourbeau@cogeco.com
(514) 874-2600 extension 364

TASK:	NTTF14

REFERENCE:	NTCO0324, NTCO0331, NTCO0333, NTCO0334, NTCO0336, and NTRE035

Notice:

This contribution has been prepared by Cogeco Cable Inc. to assist the Network Working Group in the development of an IP-to-IP interconnection interface guideline (TIF14). This should not be construed as a binding proposal by Cogeco Cable Inc. Specifically, Cogeco Cable Inc. reserves the right to make amendments, modifications or withdraw this contribution at any time.

# BACKGROUND

- In its decision 97-8 and 2005-28 the CTRC directs service providers under its jurisdiction to address VoIP interconnection:

“In Telecom Decision CRTC 97-8, Local Competition, the Commission encouraged efficient, technologically neutral interconnection arrangements of competing networks to the benefit of all subscribers. Given that the ILECs and other service providers are already deploying VoIP technology and that this trend is expected to continue, the Commission considered that, for reasons including improved network efficiency, standardized IP-to-IP interconnection is an important issue that needs to be resolved as IP becomes more prevalent in the market.

The Commission noted that CISC had already undertaken the task of developing IP-to-IP interconnection interface guidelines.  While MTS Allstream had requested that instead of delegating this issue to CISC, the Commission be directly involved in matters related to IP interconnection, the Commission decided that it should first review the guidelines issued by CISC and then determine any further course of action, as required.”

Task NTTF014 which has the objective of developing an IP-to-IP interconnection interface guideline was created and considers the following:

- Interconnection between telephony service providers under the jurisdiction of the CRTC.

- The functionalities of the approved CCS7 minimum message set.

- Service functionalities to be supported and the information that needs to be exchanged across the network-to-network interface and the functionalities of the approved CCS7 minimum message set.

- IP standards and protocols that are commonly used for carrier-to-carrier interconnections.  The initial focus will be on the Session Initiation Protocol, but other protocols will not be excluded.  Carrier specific implementation requirements will not be considered in this TIF.

- Relevant standards-developing bodies and current IP standards development processes within these standard bodies.

While NTRE035 addresses mainly point number two and four of NTTF014 objectives, this contribution focuses on point number three as a next logical step in the establishment of an IP-to-IP interconnection interface guideline.

# INTRODUCTION

- In order to establish an IP-to-IP interconnection interface guideline that will be acceptable to all parties, a minimum set of technical default parameters has first to be agreed. Accomplishment of this task, by NTWG participants, has started by first demonstrating in NTCO0324, NTCO0331, NTCO0333, NTCO0334, and NTCO0336, that a SIP based NNI signaling protocol would support the NTWG agreed minimum SS7 message set. NTWG report NTRE035, while containing the details of this agreement, does not identify which SIP based standard is to be used nor includes all technical parameters that have to be considered.  In this regards defining a set of technical default parameters constitute the next logical step for the NTWG work on TIF14. This set of default parameters would be limited to the technical parameters necessary for successful exchange of VoIP packets and agreed minimum SS7 call features, between two or more services providers.

# EXAMPLE SCENARIO

- When trying to define an IP-to-IP interconnection interface guideline, many interconnection schemes or standards, including SIP as their base signaling protocol, will come into play. This is inherent to the nature of IP which provides an almost infinite set of possibilities in term of services or features. Some of these interconnection schemes are already standardized, while others are in the process. Most of these SIP based standards use SIP extensions, in different ways, for replication of SS7 messages and reproduction of TDM call features.

- The same thing can be anticipated for other technical parameters that have to be considered for delivery of IP-to-IP interconnection. Physical support material, such as fiber and copper, as well as quality of services (QoS) parameters, such as TOS, DIFFserv and MPLS, are part of a number of interconnection parameters that can vary from one interconnecting partner to another. Therefore, before VoIP interconnection becomes reality, all these technical parameters need to be previously negotiated and agreed upon,

- Achieving a bilateral agreement should be the basis for establishment of interconnection between two or more VoIP approved service providers. A possible start for discussion would be a minimum set of default parameters that two interconnecting parties could refer to. However if a dispute started, then the default set of technical parameters will prevail as a basis of resolution. This represents a new approach which is necessitated by the richness of IP telecommunications.

- The following table represents an example of technical default parameters. This table should be considered as a starting point for the establishment of a set of default parameters:

| OSI model | Parameters | Default |
| --- | --- | --- |
| Layer 5 and above | NNI signaling | Basic Signaling: SIP 2.0 (RFC3261) + Extensions: RFC(3325)& draft-levy-sip-diversion-08.txt |
|  | Codec | G.711 μ-law |
|  | Bearer Traffic | RTP (RFC3550) RTCP (RFC3550) |
| Layer 4 | NNI signaling | Auto-negotiated between the interconnecting SIP proxies |
|  | Bearer traffic | UDP (RFC768) |
| Layer 3 | Routing protocols | BGP-4 (RFC4271) |
|  | QoS | DIFFserv (RFC2474&2475) |
|  | IP version | IPv4 (RFC791) |
| Layer 2 | VLAN | 802.1Q (IEEE) |
|  | Layer 2 QoS | 802.1p (IEEE) |
|  | Interface protocol | Ethernet (802.3z) |
|  | Interface Speed | GiGEthernet (Minimum Value) |
| Layer 1 | Interface transport | Single-Mode Fiber |

# CONCLUSION

- Having a default set of technical parameters, defining an IP-to-IP interface, would greatly facilitates VoIP interconnection and facilitate the dispute resolution mechanism by defining the basis of discussion, while following an agreed resolution process. By considering a new approach, which corresponds more to an IP reality than a legacy TDM reality, VoIP network interconnection implementation is to become a fact of life.

# REFERENCES

- IETF RFC 3261, SIP: Session Initiation Protocol; http://www.ietf.org/rfc/rfc3261.txt?number=3261 ; June 2002

- IETF RFC 3325, Private Extensions to the Session Initiation Protocol (SIP) for Asserted Identity within Trusted Networks; http://www.ietf.org/rfc/rfc3325.txt?number=3325 ; November 2002

- IETF RFC 3550, RTP: A Transport Protocol for Real-Time Applications; http://www.ietf.org/rfc/rfc3550.txt?number=3550 ; July 2003

- IETF RFC 768, User Datagram Protocol; http://www.apps.ietf.org/rfc/rfc768.html ; August 1980

- IETF RFC 4271, A Border Gateway Protocol 4 (BGP-4); http://www.ietf.org/rfc/rfc4271.txt?number=4271 ; January 2006

- IETF RFC 1812, Requirements for IP Version 4 Routers; http://www.ietf.org/rfc/rfc1812.txt?number=1812 ; June 1995

- IETF RFC 2474, Definition of the Differentiated Services Field (DS Field) in the IPv4 and IPv6 Headers; http://www.ietf.org/rfc/rfc2474.txt?number=2474 ; December 1998

- IETF RFC 2475, An Architecture for Differentiated Services; http://www.ietf.org/rfc/rfc2475.txt?number=2475 ; December 1998

- IETF RFC 791, INTERNET PROTOCOL DARPA INTERNET PROGRAM PROTOCOL SPECIFICATION;  http://www.apps.ietf.org/rfc/rfc791.html ; September 1991

- IETF, Diversion Indication in SIP draft-levy-sip-diversion-08.txt, http://www.softarmor.com/wgdb/docs/draft-levy-sip-diversion-08.txt ; August 2004

- IEEE, 802.1Q; EEE Standards for Local and metropolitan area networks—Virtual Bridged Local Area Networks;  http://standards.ieee.org/catalog/olis/lanman.html#bridging ; 2003

- IEEE, 802.1p; EEE Standards for Local and metropolitan area networks—Virtual Bridged Local Area Networks;  http://standards.ieee.org/catalog/olis/lanman.html#bridging ; 2003

- IEEE, 802.3z; CSMA/CD Access Method (802.3); http://standards.ieee.org/catalog/olis/lanman.html#bridging

*** End of Document ***

# Footnotes

DIFFserv values for RTP, RTCP and SIP signaling to be specified by the NTWG in the IP-to-IP interface      guideline.

May be discarded by common agreement of interconnecting partners. To be used when multiple interconnection partners meet at the same peering point.

May be discarded by common agreement of interconnecting partners. To be used when multiple interconnection partners meet at the same peering point and use layer 2 only for interconnection to multiple partners in the same POI. 802.1p COS values for RTP, RTCP and SIP signaling to be specified by the NTWG in the IP-to-IP interface guideline.

The minimum interconnection speed would be 1 GiGEthernet. Upgrade to many GiGEthernet will be done when the current VoIP interconnection interface is at 80% of its total capacity. Multiple GiGE must work in load sharing mode otherwise upgrading to a 10GiGEtherent becomes mandatory.

Upon common agreement by interconnecting partners, Multi-Mode Fiber could be used. A good example of such a situation would be when interconnecting partners (POI) are in the same building.